NOTIFICATION

The following notification is being circulated in accordance with Article 10.6

| 1. | Notifying Member: Canada If applicable, name of local government involved (Article 3.2 and 7.2): |
| --- | --- |
| 2. | Agency responsible: Environment Climate Change Canada Name and address (including telephone and fax numbers, email and website addresses, if available) of agency or authority designated to handle comments regarding the notification shall be indicated if different from above: Canada's Notification Authority and Enquiry Point Technical Barriers and Regulations Division Global Affairs Canada 111 Sussex Drive Ottawa (Ontario) K1A 0G2 Canada Telephone: (343)203-4273 Fax: (613)943-0346 E-mail: enquirypoint@international.gc.ca |
| 3. | Notified under Article 2.9.2 [X], 2.10.1 [ ], 5.6.2 [X], 5.7.1 [ ], other: |
| 4. | Products covered (HS or CCCN where applicable, otherwise national tariff heading. ICS numbers may be provided in addition, where applicable): Fuel (HS: 271012 and 271019); Quality (ICS 03.120), Environmental protection (ICS 13.020), Fuels (ICS 75.160) |
| 5. | Title, number of pages and language(s) of the notified document: Clean Fuel Regulations (323 pages, available in English and French) |
| 6. | Description of content: The proposed Clean Fuel Regulations (the proposed Regulations) would require primary suppliers (i.e., liquid fossil fuel producers and importers) to reduce the carbon intensity (CI) of the liquid fossil fuels they produce and import in Canada from 2016 CI levels by 2.4gCO2e/MJ in 2022, increasing to 12gCO2e/MJ in 2030. The proposed Regulations would also establish a credit market whereby the annual CI reduction requirement could be met via three main categories of credit-creating actions: actions throughout its lifecycle of fossil fuels that reduce the CI of the fossil fuel, supplying low-carbon fuels, and specified end-use fuel switching in transportation. Parties that are not primary suppliers would be able to participate in the credit market as voluntary credit creators (e.g., low carbon intensity fuel producers and importers). In addition, the proposed Regulations would include the minimum volumetric requirements (minimum 5% low CI fuel content in gasoline and 2% low CI fuel content in diesel fuel and light fuel oil) currently set out in the federal Renewable Fuel Regulations. A Fuel LCA Model is being developed to support the development and implementation of the proposed Regulations. Low carbon intensity fuel producers would be permitted to use the model to determine facility specific CI values once 24 months of operating data is available. The propose Regulations will increase the use of biofuels in Canada and the demand for biofuel feedstock. Only biofuels made from biomass feedstock that adhere to land use and biodiversity criteria will be eligible for compliance credit creation. These criteria ensure the financial incentives created by the Regulations do not result in loss of biodiversity or negative land use impacts from growing and harvesting biofuel feedstock. These criteria apply to feedstock regardless of geographic origin. A primary supplier may also choose avail of the compliance fund mechanism by contributing to a funding program in order to satisfy up to 10% of its annual reduction requirement. Funds or programs within a fund that reduce CO2e emissions may be eligible to become registered funds, the fund must provide funding for projects or activities that support the deployment or commercialization of technologies or processes that reduce CO2e emissions. For primary suppliers who are unable to satisfy their reduction requirement by 30 June following the end of a given compliance period, a market clearing mechanism that facilitates credit acquisition by primary suppliers would also be implemented. The majority of applications and reports must be submitted with a validation or verification statement that pertains to the validity of the application / report. The validation / verification body must have the appropriate accreditations as well as the application / report being reviewed by an independent reviewer. |
| 7. | Objective and rationale, including the nature of urgent problems where applicable: The proposed Regulations intend to reduce GHG emissions by reducing the lifecycle CI of liquid fossil fuels used in Canada. This would be achieved through a flexible, regulatory approach towards GHG reduction that would incentivize low-carbon fuel uptake, end-use fuel switching in transportation, and process improvements in the oil and gas sector. The proposed Regulations would work in conjunction with other federal, provincial and territorial policies to contribute towards the Pan-Canadian Framework helping to achieve Canada's 2030 Paris target. The proposed Regulations would encourage innovation and growth by increasing the likelihood of technology development and adoption in an effort to help transition Canada towards a low-carbon economy; Protection of the environment |
| 8. | Relevant documents: Canada Gazette, Part I, 19 December 2020, pages 3868 to 4191 (available in English and French) |
| 9. | Proposed date of adoption: Normally within 12 months of publication in the Canada Gazette, Part I. Proposed date of entry into force: These regulations would come into force the day on which they are registered. Reduction requirements for primary suppliers would come into force on 1 December 2022. |
| 10. | Final date for comments: 4 March 2021 |
| 11. | Texts available from: National enquiry point [X] or address, telephone and fax numbers and email and website addresses, if available, of other body: The electronic version of the regulatory text can be downloaded at: http://www.gazette.gc.ca/rp-pr/p1/2020/2020-12-19/html/reg2-eng.html http://www.gazette.gc.ca/rp-pr/p1/2020/2020-12-19/html/reg2-fra.html |